## Slide 1: Importance of N2Hx Reaction Pathways in Modelling of NH3/H2/Air Flame Chemistry
Department of Mechanical Engineering, Reactive Gas Dynamics
UROTHIYIL Aahil Ashraf
2026年11月8日

## Slide 2
Ammonia combustion is a growing area of research as a carbon-free alternative to traditional fuels.
Numerically simulating ammonia blends is necessary for studying combustion properties and developing combustion systems.
Large-scale modelling with detailed chemical kinetics mechanisms increases computational cost.
Reduced chemical kinetic mechanisms optimized for multiple ammonia blends and operating conditions is needed.
Notes: Include importance of ammonia combustion simulation
for emission control etc
Lesser whitespace
Figures relevant to talking points

## Slide 3
Existing reduced chemical kinetics mechanisms target specific fuel blends for select operating conditions.
Elucidating reaction pathways particular to specific fuel blends helped develop a kinetics mechanism viable for a wider range of fuels.
Notes: Change images; unclear as to what the image represents

## Slide 4
Develop a reduced kinetic mechanism optimized for NH3, NH3/CH4 and NH3/H2
  Prioritizing unstretched laminar burning velocity predictions
  Viable for cases with varying pressure and equivalence ratio
Validate the Present Mechanism with experimental flame speed measurements from literature

## Slide 5
Present mechanism is based on the reduced mechanism developed by Okafor et al. (2019).
  This mechanism is developed to model laminar burning velocities of NH3/air and NH3/CH4/air flames accurately.
  The mechanism is not optimized for NH3/H2/air flames.
    Hence underpredicts flame speed when H2 concentration exceeds
Underlying chemistry in NH3/H2/air flames were studied by studying reaction mechanisms developed for this blend.
  Reaction mechanism by Gotama et al. (2022) was optimized for laminar burning velocity of NH3/H2/air flames.
Notes: Okafor mech fails nh3/h2 lbv modeling because mech not developed for this blend
Explain why gotama mech selected
“a reaction mechanism developed for nh3/h2 flame selected to STUDY nh3/h2 flame chemistry”
Don’t say compare. Emphasis on how other mechanisms were used to study the chemistry.

## Slide 6
Unstretched laminar burning velocity, , of premixed flames calculated with 1D unstretched adiabatic simulations
  Premixed Laminar Flame Speed Calculation model in ANSYS Chemkin-PRO used
  Computational domain of 10 cm
  Adaptive grid settings GRAD and CURV set to 0.01
Notes: Operating conditions selected because substantial experimental data exists for this condition in literature

## Slide 7: Experimental Data-points for of NH3/H2/air Flames
Most experimental data available at 1 atm of pressure
Stoichiometric ( equivalence ratio has the most data points
To evaluate reaction mechanisms pressure of 1 atm and equivalence ratio of selected

## Slide 8
Figure: Experimental and numerical laminar burning velocity of NH3/H2/air flames under stoichiometric condition at various hydrogen concentrations.
Notes: Include okafor detailed mechanism in the figure
Mention how there is an underlying misrepresentation in okafor mech leading to nh3/h2 lbv underprediction

## Slide 9
Normalized sensitivity of to rate constants of elementary reactions highlighted reactions with significant effect on .
Mechanisms were studied using reaction pathways constructed with integrated rate of production (IROP) of major NH3 and H2 oxidation species.
IROP was calculated with the equation:
Flame used for the analyses had hydrogen concentration of .
Notes: Include use of sensitivity analysis to determine reactions important to lbv

## Slide 10: Sensitivity Analysis of

## Slide 11
Okafor Reduced Mech
Gotama Mech
Unimolecular
Unimolecular
Notes: Replace (a) and (b) to names of mechanism
Remove caption

## Slide 12: Key Findings from Reaction Pathway Analysis
NH2 N2Hx pathways play a significant role in formation and consumption of N2Hx species.
Okafor Reduced Mech
Gotama Mech

## Slide 13: Key Findings from Reaction Pathway Analysis
NH2 N2Hx pathways play a significant role in formation and consumption of N2Hx species.
Present Mech was updated to model these pathways more accurately.
Elementary Reaction | Okafor Reduced Mech |  |  | Present Mech |  |  | Source
NH+NH=N2H2 |  |  |  | 6.26E+13 | -0.036 | -161.00 | S.J. Klippenstein, et al. (2009)
NH2+NH2=N2H2+H2 |  |  |  | 7.83E+11 | 0.000 | 0.00 | N. Stothard, et al. (1995)
N2H2+NH=NNH+NH2 |  |  |  | 2.40E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+NO=N2O+NH2 |  |  |  | 4.00E+12 | 0.000 | 11922.00 | A.M. Dean, et al. (2000)
N2H3+NH2=N2H2+NH3 |  |  |  | 9.20E+05 | 1.940 | -1152.00 | A.M. Dean, et al. (2000)
NH2+NH<=>N2H2+H | 5.00E+13 | 0.000 | 0.00 | 4.30E+14 | -0.272 | -77.00 | S.J. Klippenstein, et al. (2009)
NH2+NH=N2H2+H | 5.00E+13 | 0.000 | 0.00 |  |  |  | 
Elementary Reaction | Okafor Reduced Mech |  |  | Present Mech |  |  | Source
NH+NH=N2H2 |  |  |  | 6.26E+13 | -0.036 | -161.00 | S.J. Klippenstein, et al. (2009)
NH2+NH2=N2H2+H2 |  |  |  | 7.83E+11 | 0.000 | 0.00 | N. Stothard, et al. (1995)
N2H2+NH=NNH+NH2 |  |  |  | 2.40E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+NO=N2O+NH2 |  |  |  | 4.00E+12 | 0.000 | 11922.00 | A.M. Dean, et al. (2000)
N2H3+NH2=N2H2+NH3 |  |  |  | 9.20E+05 | 1.940 | -1152.00 | A.M. Dean, et al. (2000)
NH2+NH<=>N2H2+H | 5.00E+13 | 0.000 | 0.00 | 4.30E+14 | -0.272 | -77.00 | S.J. Klippenstein, et al. (2009)
NH2+NH=N2H2+H | 5.00E+13 | 0.000 | 0.00 |  |  |  | 

## Slide 14: Key Findings from Reaction Pathway Analysis
N2H2 formed contributes to the formation of NNH
  Primarily through the decomposition of N2H2
Chart: 
| N2H2+H<=>NNH+H2 | N2H2+NH2<=>NNH+NH3 | N2H2+NH<=>NNH+NH2 | N2H2+O<=>NNH+OH | N2H2+OH<=>NNH+H2O | NH2+NO<=>NNH+OH | N2+H+O2<=>NNH+O2 | N2+HO2<=>NNH+O2 | NNH+O<=>N2O+H | NH+NO<=>NNH+O | N2+H<=>NNH
Gotama Mech | 2.5967e-05 | 5.5732e-07 | 2.7723e-07 | 2.0881e-06 | 2.0986e-06 | 1.2588e-05 | 1.0951e-06 | 5.6729e-07 | -2.29e-06 | -4.5189e-05
Okafor Reduced Mech | 8.3124e-06 | 1.2242e-06 | 1.17e-06 | 7.692e-06 | 2.1068e-06 | 8.494e-06 | 5.9496e-07 | -1.8603e-06 | -1.0253e-05

## Slide 15: Key Findings from Reaction Pathway Analysis
Present Mech was updated with rate constants below to model these pathways.
Elementary Reaction | Okafor Reduced Mech |  |  | Present Mech |  |  | Source
N2H2+NH=NNH+NH2 |  |  |  | 2.40E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+NH2=NNH+NH3 |  |  |  | 8.80E-02 | 4.050 | -1610.00 | D.P. Linder, et al. (1996)
N2H2+H=NNH+H2 | 8.50E+04 | 2.630 | 230.00 | 1.10E+14 | 0.000 | 3128.00 | P. Glarborg, et al. (2018)
N2H2+OH=NNH+H2O | 5.90E+01 | 3.400 | 1363.00 | 5.90E+01 | 3.400 | -1363.00 | D.P. Linder, et al. (1996)
Elementary Reaction | Okafor Reduced Mech |  |  | Present Mech |  |  | Source
N2H2+NH=NNH+NH2 |  |  |  | 2.40E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+NH2=NNH+NH3 |  |  |  | 8.80E-02 | 4.050 | -1610.00 | D.P. Linder, et al. (1996)
N2H2+H=NNH+H2 | 8.50E+04 | 2.630 | 230.00 | 1.10E+14 | 0.000 | 3128.00 | P. Glarborg, et al. (2018)
N2H2+OH=NNH+H2O | 5.90E+01 | 3.400 | 1363.00 | 5.90E+01 | 3.400 | -1363.00 | D.P. Linder, et al. (1996)

## Slide 16: Key Findings from Reaction Pathway Analysis
NNH is consumed primarily through its decomposition to produce H radicals.
Chart: 
| N2H2+H<=>NNH+H2 | N2H2+NH2<=>NNH+NH3 | N2H2+NH<=>NNH+NH2 | N2H2+O<=>NNH+OH | N2H2+OH<=>NNH+H2O | NH2+NO<=>NNH+OH | N2+H+O2<=>NNH+O2 | N2+HO2<=>NNH+O2 | NNH+O<=>N2O+H | NH+NO<=>NNH+O | N2+H<=>NNH
Gotama Mech | 2.5967e-05 | 5.5732e-07 | 2.7723e-07 | 2.0881e-06 | 2.0986e-06 | 1.2588e-05 | 1.0951e-06 | 5.6729e-07 | -2.29e-06 | -4.5189e-05
Okafor Reduced Mech | 8.3124e-06 | 1.2242e-06 | 1.17e-06 | 7.692e-06 | 2.1068e-06 | 8.494e-06 | 5.9496e-07 | -1.8603e-06 | -1.0253e-05

## Slide 17: Key Findings from Reaction Pathway Analysis
Increased formation of NNH yields an increased contribution to H radical production.
Chart: 
| 2NH2<=>N2H3+H | O+OH<=>H+O2 | H2+NO<=>HNO+H | NO+H2<=>HNO+H | NNH+H2<=>N2H2+H | N2H3+M<=>N2H2+H+M | N2+OH<=>N2O+H | NH+H2<=>NH2+H | N+H2<=>NH+H | NH+NO<=>N2O+H | NH2+NH<=>N2H2+H | NH2+O<=>HNO+H | NH2+H2<=>NH3+H | NNH<=>N2+H | O+H2<=>H+OH | OH+H2<=>H+H2O
Gotama Mech | -2.343e-05 | 0.00024936 | 3.3077e-05 | 2.5967e-05 | -5.7801e-05 | 2.828e-05 | 2.2767e-05 | 4.5189e-05 | 0.00011493 | 0.00025196
Okafor Reduced Mech | 0.00015179 | 3.4571e-05 | -7.9838e-05 | 1.6681e-05 | 4.7112e-05 | 1.8355e-05 | 3.216e-05 | 1.7796e-05 | 5.4956e-05 | 0.00020318

## Slide 18: Updates in Present Mechanism
Elementary Reaction | Okafor Reduced Mech |  |  | Present Mech |  |  | Source
NH+NH=N2H2 |  |  |  | 6.26E+13 | -0.036 | -161.00 | S.J. Klippenstein, et al. (2009)
NH2+NH2=N2H2+H2 |  |  |  | 7.83E+11 | 0.000 | 0.00 | N. Stothard, et al. (1995)
NH2+NH2=N2H2+H2 |  |  |  | 7.83E+11 | 0.000 | 0.00 | N. Stothard, et al. (1995)
N2H2+NH=NNH+NH2 |  |  |  | 2.40E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+NH2=NNH+NH3 |  |  |  | 8.80E-02 | 4.050 | -1610.00 | D.P. Linder, et al. (1996)
N2H3+NH2=N2H2+NH3 |  |  |  | 9.20E+05 | 1.940 | -1152.00 | A.M. Dean, et al. (2000)
N2H2+NO=N2O+NH2 |  |  |  | 4.00E+12 | 0.000 | 11922.00 | A.M. Dean, et al. (2000)
N2H3+O=N2H2+OH |  |  |  | 1.70E+08 | 1.500 | -646.00 | A.M. Dean, et al. (2000)
N2H3+OH=N2H2+H2O |  |  |  | 1.20E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+H=NNH+H2 | 8.50E+04 | 2.630 | 230.00 | 1.10E+14 | 0.000 | 3128.00 | P. Glarborg, et al. (2018)
N2H2+OH=NNH+H2O | 5.90E+01 | 3.400 | 1363.00 | 5.90E+01 | 3.400 | -1363.00 | D.P. Linder, et al. (1996)
NH2+NH<=>N2H2+H | 5.00E+13 | 0.000 | 0.00 | 4.30E+14 | -0.272 | -77.00 | S.J. Klippenstein, et al. (2009)
NH2+NH=N2H2+H | 5.00E+13 | 0.000 | 0.00 |  |  |  | 
N2H3+M=N2H2+H+M | 2.00E+16 | 0.000 | 37000.00 |  |  |  | 
N2H3+HO2=N2H2+H2O2 | 1.40E+04 | 2.690 | -1600.00 |  |  |  | 
Elementary Reaction | Okafor Reduced Mech |  |  | Present Mech |  |  | Source
NH+NH=N2H2 |  |  |  | 6.26E+13 | -0.036 | -161.00 | S.J. Klippenstein, et al. (2009)
NH2+NH2=N2H2+H2 |  |  |  | 7.83E+11 | 0.000 | 0.00 | N. Stothard, et al. (1995)
NH2+NH2=N2H2+H2 |  |  |  | 7.83E+11 | 0.000 | 0.00 | N. Stothard, et al. (1995)
N2H2+NH=NNH+NH2 |  |  |  | 2.40E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+NH2=NNH+NH3 |  |  |  | 8.80E-02 | 4.050 | -1610.00 | D.P. Linder, et al. (1996)
N2H3+NH2=N2H2+NH3 |  |  |  | 9.20E+05 | 1.940 | -1152.00 | A.M. Dean, et al. (2000)
N2H2+NO=N2O+NH2 |  |  |  | 4.00E+12 | 0.000 | 11922.00 | A.M. Dean, et al. (2000)
N2H3+O=N2H2+OH |  |  |  | 1.70E+08 | 1.500 | -646.00 | A.M. Dean, et al. (2000)
N2H3+OH=N2H2+H2O |  |  |  | 1.20E+06 | 2.000 | -1192.00 | A.M. Dean, et al. (2000)
N2H2+H=NNH+H2 | 8.50E+04 | 2.630 | 230.00 | 1.10E+14 | 0.000 | 3128.00 | P. Glarborg, et al. (2018)
N2H2+OH=NNH+H2O | 5.90E+01 | 3.400 | 1363.00 | 5.90E+01 | 3.400 | -1363.00 | D.P. Linder, et al. (1996)
NH2+NH<=>N2H2+H | 5.00E+13 | 0.000 | 0.00 | 4.30E+14 | -0.272 | -77.00 | S.J. Klippenstein, et al. (2009)
NH2+NH=N2H2+H | 5.00E+13 | 0.000 | 0.00 |  |  |  | 
N2H3+M=N2H2+H+M | 2.00E+16 | 0.000 | 37000.00 |  |  |  | 
N2H3+HO2=N2H2+H2O2 | 1.40E+04 | 2.690 | -1600.00 |  |  |  | 

## Slide 19
Figure: Experimental and numerical laminar burning velocity of NH3/H2/air flames under stoichiometric condition at various hydrogen concentrations.

## Slide 20: Validation – NH3/H2/air
Figure 1: Comparison of measured and simulated laminar burning velocity of NH3/H2/air flames under lean condition and 1 atm of pressure.
Figure 2: Comparison of measured and simulated laminar burning velocity of NH3/H2/air flames under rich condition and 1 atm of pressure.
Notes: Unable to validate for elevated pressures due to a lack of experimental data

## Slide 21: Validation – NH3/CH4/air
Figure: Comparison of measured and simulated laminar burning velocity of NH3/CH4/air flames under stoichiometric condition and 1 atm of pressure.
Notes: Make sure graph starts at 0,0
Explain why N2Hx pathways do not affect nh3/ch4 flames

## Slide 22: Validation – NH3/CH4/air